## Slide 1: Sustainability- Principles and Practices
Chapter 11
Construction Industry to Sustainability

## Slide 2: LEARNING OBJECTIVES
Explain the levels of LEED certification
Discuss how using LEED standards will lower the ecological footprint
Describe the LEED credit weighting process
Describe how a green roof saves energy
Discuss the meaning of a passive house
Discuss the advantages of using recycled and local materials
Describe why thermal controls are needed
Explain how using natural light and LED lighting helps sustainability
Discuss how using CMMS (Computerized Maintenance Management Systems) helps control costs

## Slide 3: INTRODUCTION
Opportunities In Construction
  Apply principles of sustainability
  End waste/abuse improve carbon footprint
    Through conservation and reuse
  USGBC, US Green Building Council
    Developed
      LEED (LEADERSHIP IN ENERGY & ENVIRONMENTAL DESIGN)
      Rating systems: design, construction, operation, maintenance
      Green buildings, homes, & neighborhoods

## Slide 4: LEED (LEADERSHIP IN ENERGY & ENVIRONMENTAL DESIGN) 1.
LEED (LEADERSHIP IN ENERGY & ENVIRONMENTAL DESIGN)
  Worldwide green building certification program
    USGBC or U.S. Green Building Council
    Rating systems
    501(c) 3 non-profit membership based organization
    Promotes sustainability
What is LEED: 5:50
LEED Credits for Energy Modelers: 1:12

## Slide 5: FIGURE 11-1 tower PNC building in Pittsburg that is LEED certified

## Slide 6: LEED (LEADERSHIP IN ENERGY & ENVIRONMENTAL DESIGN) 2.
LEED Progress
  Grew from a single building standard
  To all-inclusive system of interrelated standards
  Cover all phases from design to maintenance & operation

## Slide 7: LEED GREEN BUILDING RATING SYSTEM 1.
LEED Versions:
  LEED NC version 2.0,
  LEED NC version 2.2 in 2005
  LEED 2009 (previously named LEED Version 3)
  LEED version 4, 11/2013 to 10/2016
  Choose between LEED 2009 and LEED Version 4
  Projects registering after October 31, 2016
  Must use LEED Version 4

## Slide 8: LEED GREEN BUILDING RATING SYSTEM 2.
5 Predominant Categories
  LEED professional construction program:
    Green Building Design & Construction
    Green Interior Design & Construction
    Green Building Operations & Maintenance
    Green Neighborhood Development
    Green Home Design and Construction

## Slide 9: FIGURE 11-2 Taipei 101, tallest and largest green building of LEED Platinum certification in world since 2011

## Slide 10: LEED GREEN BUILDING RATING SYSTEM 3.
LEED 2009
  100 possible base points distributed
    Across 6 credit categories
    Sustainable Sites, Water Efficiency, Energy, Atmosphere, Materials and Resources, Indoor Environmental Quality, & Innovation in Design
    10 additional points may be earned
    4 additional points for Regional Priority Credits
    6 additional points for Innovation in design

## Slide 11: LEED GREEN BUILDING RATING SYSTEM 4.
Certification Level
  4 Different LEED Certification Levels:
    Certified: 40–49 points
    Silver: 50–59 points
    Gold: 60–79 points
    Platinum: 80 points & above
Figure 11-3 LEED Certification Levels
How to get LEED Certified: 2:22

## Slide 12: LEED GREEN BUILDING RATING SYSTEM 5.
LEED 2009 Performance Credit System
  Assign points based on environmental impacts
  Human benefits of each credit
  EPA's Tools Reduction and Assessment of Chemical and Other Environmental Impacts (TRACI)
  Developed by National Institute of Standards & Technology (NIST).

## Slide 13: LEED GREEN BUILDING RATING SYSTEM 6.
Figure 11-4 Requirements
  To participate in LEED 2009
    Building must comply with environmental laws and regulations, occupancy scenarios, building permanence and pre-rating completion, site boundaries and area-to-site ratios

## Slide 14: LEED GREEN BUILDING RATING SYSTEM 7.
Number of Points Project Earns
  Determines its level of LEED certification categories:
    Innovation in Design
    Indoor Environmental Quality
    Sustainable Sites
    Water Efficiency
    Energy & Atmosphere
    Materials and Resources
    Regional Priority

## Slide 15: LEED GREEN BUILDING RATING SYSTEM 8.
LEEDS Credit Weighting Process
  Following 3 steps:
    Collection of reference buildings are used to determine environmental impacts of any building seeking LEED certification
    National Institute of Standards and Technology weightings are used to judge importance of these impacts in each category
    Data regarding actual impacts on environmental and human health used to assign points to individual categories &metrics

## Slide 16: LEED GREEN BUILDING RATING SYSTEM 9.
LEEDS Environmental Impact
  Use same source energy
    Produce equal greenhouse gas emissions
    As non-LEED-certified buildings
  However, use between 11% and 39% less site energy
    Than non-LEED buildings
  Reduces ecological footprint

## Slide 17: FIGURE 11-5 Green Building Information Gateway (GBIG) is a web-based tool, search engine and data platform for exploring and comparing the green dimensions of the built environment

## Slide 18: LEED GREEN BUILDING RATING SYSTEM 10.
GBIG Categories Available With Tool:
  Activities
  Buildings
  Places
  Strategies
  Collections

## Slide 19: QUESTION 1:
LEED (Leadership in Energy & Environmental Design) is a worldwide green building certification program that was developed by?
a. EPA (environmental Protection Agency)
b. USGBC (US Green Building Council
c. DOE (US Department of Energy)
d. The UN (United Nations)

## Slide 20: ANSWER 1:
USGBC (US Green Building Council

## Slide 21: QUESTION 2:
How many points or credit are need for LEED Gold certification?
a. 40–49 points
b. 50–59 points
c. 60–79 points
d. 80 points and above

## Slide 22: ANSWER 2:
60–79 points

## Slide 23: STUDENT ACTIVITY 1.
Download WORD file: LEED (Leadership in Energy & Environmental Design) Certification

## Slide 24: BREEAM 1.
BREEAM (Building Research Establishment Environmental Assessment Method)
  Longest established method of assessing, rating
  Certifying sustainability of buildings
  Raise awareness among builders and owners
  Benefits of taking a sustainability approach

## Slide 25: BREEAM 2.
BREEAM Assesses
  energy and water use, health, pollution, transportation, materials, waste, ecology and management processes
Figure 11-6 BREEAM Weightings

## Slide 26: GREEN (LEED) CONSTRUCTION 1.
Green Roof (Figure 11-7)
  Living building roof
    Partially or completely covered with vegetation
      Growing medium, planted over waterproofing membrane
      Root barrier and drainage and irrigation systems
      They serve several purposes including:
        absorbing rainwater
        providing insulation
        creating a habitat for wildlife
        Aesthetically pleasing landscape
        Lower urban air temperatures

## Slide 27: FIGURE 11-7 Green Roof

## Slide 28: GREEN (LEED) CONSTRUCTION 2.
Green Roof
  Serve several purposes including:
    Absorbing rainwater
    Providing insulation
    Creating a habitat for wildlife
    More aesthetically pleasing landscape
    Helping to lower urban air temperatures
    Mitigate heat island effect
Green Roofs Save Energy (Speaker): 6:22

## Slide 29: GREEN (LEED) CONSTRUCTION 3.
Green Roof Advantages
  Reducing Energy use
    Reducing heating & cooling by 50-90%
  Extend lifespan of a roof by over 200%
    Waterproofing membrane with growing medium
  Lifespan of roof 3 times after greening roof
  Increase real estate value by about 7%.
  Stormwater tax reduction, grants, or rebates.
  Reduce Carbon Dioxide (CO2) emissions

## Slide 30: GREEN (LEED) CONSTRUCTION 4.
Green Roof Disadvantages
  Initial cost of installing a green roof can be double
  Large strain on the structural support of a building
  More maintenance and maintenance energy
    Compared to a standard roof

## Slide 31: FREQUENTLY ASKED QUESTION?
How Does Green Roof Reduce NOx, Particulate Matter & CO2 emissions?
  Nitrogen-oxides (NOx) and particulate matter (PM) is produced in combustion and creates smog and acid rain. Plants remove these pollutants from the air through their pores, or stomates. Thicker growth medium or growth medium on a green roof that includes expanded clays and shales can allow a roof to remove or absorb large amounts of carbon dioxide. Plants like large perennials can also increase a roof’s ability to absorb carbon, while the application of fertilizer, composition of growth medium and irrigation can also have an effect

## Slide 32: QUESTION 3:
Which of these is a living building top that is partially or completely covered with vegetation and a growing medium, planted over a waterproofing membrane?
a. Solar panel roof
b. Green roof
c. Passive house
d. Geothermal roof

## Slide 33: ANSWER 3:
Green roof

## Slide 34: STUDENT ACTIVITY 4.
Download WORD file: Green Building Best Practices

## Slide 35: PASSIVE HOUSE 1.
Passive House
  Voluntary standard for energy efficiency
  Reducing its ecological footprint
    MINERGIE-P, is used in Switzerland Standard
  Not confined to residential properties
  Design process integrated with architectural design
  Applied to new buildings & renovation projects
Passive House Explained in 90 Seconds: 1:35

## Slide 36: FIGURE 11-8 Passive House

## Slide 37: PASSIVE HOUSE 2.
Passive House Standard
  Annual heating and cooling demand
  Not more than 4,755 BTU/square foot per year
  Peak heat load of 10 watts per square meter
  Total primary energy
    Not be more than 38,040 BTU/ square foot per year.
  Not leak more air than 0.6 times
    House volume per hour as tested by a blower door
    Leakage rate must be < 0.05 cubic feet per minute

## Slide 38: PASSIVE HOUSE 3.
Recycled and Local Construction Materials
  Recyclables remanufactured for reuse
  Include many kinds of construction materials
  Demolition materials are materials left over:
    Concrete
    Wood
    Drywall
    Asphalt shingles
    Asphalt pavement
    Metal
Recycled Glass: 4:24

## Slide 39: ENERGY EFFICIENT HOUSE

## Slide 40: HOME AIR LEAKAGE
NO ANIMATION IN FOLDER

## Slide 41: THERMAL CONTROLS 1.
Thermal Control
  Used in almost all buildings to achieve comfort
  Useful for assessing energy use
  Requires insulation layers
  Few thermal bridges
  Effective air barrier system
  Good control of radiation
  Management of interior heat generation
  Forms of renewable green energy

## Slide 42: FIGURE 11-9 Controls for thermal comfort are sensors and controllers, such as thermostats, humidistats, mechanized blinds, mechanized windows or ventilation openings, and other building automation systems like energy management dashboard, which keeps the environment within comfortable temperature and humidity values.

## Slide 43: THERMAL CONTROLS 2.
Basic and Advanced Systems
  Climate control systems
    Individual controllers for different products
    System that connects all sensors and controllers
    Unified systems can incorporate controls for
      Lighting, indoor air quality, and water

## Slide 44: Figure 11-10 Heat pump thermal storage system

## Slide 45: THERMAL CONTROLS 3.
Predicting People Comfort Needs
  Predictable occupancy and activity schedules
  Use advanced artificial intelligence to predict needs
Figure 11-11 motion sensor
When occupancy is less predictable, motion sensors can be used to determine whether someone is in the room.

## Slide 46: THERMAL CONTROLS 4.
Smart Phone Control
  Anticipated occupancy is not possible
  Remote mobile apps for a smart phone
  Web-based controls can be used
Figure 11-12 smart phone mobile app for HVAC

## Slide 47: THERMAL CONTROLS 5.
Sustainability and Lighting
  Using daylight in design of building
    Justified for a number of reasons
    Increases in productivity
      Regulates melatonin production in the pineal gland
        Which regulates sleep
      Daylight used in appropriate quantities to light interior spaces
      Will reduce dependence on electric lighting

## Slide 48: FIGURE 11-13 A light shelf is a daylight delivery system that is used to reflect daylight to the ceiling and decrease daylight levels adjacent to a window.

## Slide 49: THERMAL CONTROLS 6.
Sustainability Lights
  LED (Light Emitting Diode)
    Voltage applied to leads, electrons recombine with electron holes within solid-state device releasing energy in form of photons
    Electroluminescence
    Light COLOR determined by energy band gap of semiconductor
FIGURE 11-14 LED is a two-lead semiconductor light source. It is a PN junction diode that emits light when triggered

## Slide 50: THERMAL CONTROLS 7.
LED Lighting Different
  Than incandescent & fluorescent
    Produces light very efficiently
    Electrical current passes through semiconductor
    Illuminates LED, heat absorbed into heat sink
      Common LED colors include:
        Amber
        Red
        Green
FIGURE 11-14 LED colors

## Slide 51: Figure 11-15 LED Bulbs: The useful life of LED lighting products is much higher than other light sources

## Slide 52: THERMAL CONTROLS 8.
LED Lighting Lifetime
  LED lights do not “burn out” or fail
  Lumen depreciation, where amount of light produced
  Decreases and light color appearance can change
  Useful life of LED product
  Based on prediction of when output decreases to 30%
Sustainability and LED Lighting (Ted Talk): 5:58
Light & Sustainability a Revolution: 58:41

## Slide 53: THERMAL CONTROLS 9.
Fluorescent Lamps
  Creates light by using an electric current in a gas
  Contains mercury plus other gases
  Electric current excites mercury vapor
  Causes a phosphor coating on inside of lamp to glow
    Straight and range in length from 3.9” to 8 feet
    Some tubes are bent into a circle or a U-shape
    Must use ballast to control current through lamp

## Slide 54: THERMAL CONTROLS 10.
CFL (Compact Fluorescent Lamp)
  Fluorescent lamp replaces incandescent lamp
    Tube which is curved or folded to fit into space
    Of incandescent bulb
    Compact electronic ballast in base of lamp
Figure 11-16 CFL bulb

## Slide 55: QUESTION 4:
On-Demand-Control ventilation by itself can save about how much HVAC energy?
a. 15%
b. 20%
c. 30%
d. 10%

## Slide 56: ANSWER 4:
15%

## Slide 57: CASE STUDY
Reducing Energy Costs through Lighting Changes
  Large university reduced electrical usage by changing lighting:
    Replaced conventional T8 linear fluorescent 32 watt, either 4 feet or 8 feet long tubes with 25 watt units. Saved 7 watts per bulb for a savings of about 30%.
    Standard ballasts were replaced at the same time with high-efficiency ballasts.
    Energy-efficient magnetic ballast uses copper wire coils, and the iron cores are larger. The copper has lower resistance and the larger iron core generates less heat inside the ballast.
    Some people in offices and classrooms noticed the slight decrease in the brightness of the light. The original bulbs were warm white with a light temperature of 2,800 degrees Kelvin (K) (a method used to describe the “whiteness” of the light). By using a whiter 3,500 degree lamp, the light appeared to be brighter.
    Fluorescent tubes used in tunnels in underground campus were changed to 5,000 degrees K in an effort to make these closed spaces appear to be brightly illuminated.
    These changes along amounted to a huge savings in the electrical usage

## Slide 58: STUDENT ACTIVITY 2.
Download WORD file: Sustainable Lighting Benefits

## Slide 59: STUDENT ACTIVITY 3.
Download WORD file: Sustainability and Lighting

## Slide 60: ASSET MANAGEMENT 1.
Computerized Maintenance Management System (CMMS)
  Software maintains a computer database of information
  CMMIS (Computerized Maintenance Management Information System)
  Help maintenance workers be more efficient
  Verify regulatory compliance
Maintenance Assistance CMMS: 2:11

## Slide 61: ASSET MANAGEMENT 2.
Deferred Maintenance
  Postponing maintenance activities
    Save costs, meet budget funding levels
    Failure to perform needed repairs could lead to impairment.
    May result in higher costs, asset failure, affect sustainability
    E.G.
      Putting off HVAC (Heating Ventilation and Air Conditioning System) yearly furnace cleaning
      Result in more energy consumption
      Increase building’s carbon footprint and affect sustainability

## Slide 62: ASSET MANAGEMENT 3.
Construction Operations Building Information Exchange (COBie)
  Standard relating to managed asset information
  Associated with BIM (building information modeling)
    Devised by US Army Corps of Engineers
    Capture and record important project data at point of origin
    Support operations, maintenance and asset management

## Slide 63: ASSET MANAGEMENT 4.
Reliability-Centered Maintenance (RCM)
  Process to make sure that systems
  Continue to do what their users require
  Achieve improvements in minimum levels of maintenance
  Lead to increase in cost effectiveness & reliability
  Defined by SAE (Society of Automotive Engineers)
    Standard SAE JA1011, Evaluation Criteria for RCM Processes.

## Slide 64: INTERNATIONAL FACILITY MANAGEMENT ASSOCIATION (IFMA) 1.
IFMA
  Guide and develop facility management professionals
  Providing services, products, resources, Founded as
    National Facility Management Association (NFMA)
  Not-for-profit incorporated association and
  Certifies facility managers & conducts research
  Provides educational programs
  Recognizes facility management degrees

## Slide 65: INTERNATIONAL FACILITY MANAGEMENT ASSOCIATION (IFMA) 2.
Credentialing Programs
  IFMA has 3 credentialing programs:
    Certified Facility Manager (CFM)
    Facility Management Professional (FMP)
    Sustainability Facility Professional (SFP)

## Slide 66: INTERNATIONAL FACILITY MANAGEMENT ASSOCIATION (IFMA) 3.
Operations and Maintenance (O&M) Program
  Plan of training, cleaning, work practices, and surveillance
  To Maintain asbestos-containing materials (ACM)
  Minimize exposure of all building occupants to asbestos
    EPA recommends that an O&M program include work practices to:
      Maintain ACM in good condition
      Ensure proper cleanup of asbestos fibers previously released
      Prevent further releases of asbestos fibers
      Monitor the condition of ACM

## Slide 67: INTERNATIONAL FACILITY MANAGEMENT ASSOCIATION (IFMA) 4.
LEED Maintenance Spectrum
  (LEED-EBOM [Existing Building Operations & Maintenance]) system, offers:
      Streamlined reporting
      Fewer prerequisites
      Emphasis on operations, maintenance, and upgrades
      Ease of scale for use in greening existing buildings
      High number of rewards for measured environmental performance
      Green cleaning incentives
      Strong commitment to performance
      New water efficiency credits

## Slide 68: INTERNATIONAL FACILITY MANAGEMENT ASSOCIATION (IFMA) 5.
Best Practices
  Ways to reduce operating costs and carbon emissions
  Improve energy & water performance for green buildings
  Defined as a policy, systems and procedures
  Regarded by peers as practice
  Delivers optimal outcome
  They are worthy of using

## Slide 69: INTERNATIONAL FACILITY MANAGEMENT ASSOCIATION (IFMA) 6.
Other IFMA Considerations
  Site Preparation
  Building Design
  Sustainable Materials
  Sound Construction Methods
  Environmentally Sensitive Landscaping
  Waste Management

## Slide 70: QUESTION 5:
What describes a policy, systems and procedures that, at any given time that delivers optimal outcome, such that they are worthy of using?
a. Six Sigma
b. Best practices
c. Controlled maintenance
d. Smart Budgeting

## Slide 71: ANSWER 5:
Best practices

## Slide 72: REAL PROPERTY INVENTORY (RPI) 1.
Record Of Real Property Asset
  Package for collecting/maintaining real property inventory
  Data to manage assets &meet record/reporting
  Provides data necessary to frame facility budgets
    Make decisions on facility replacement, organize repair and penalty costs, and improve the management of investments in property assets
    RPAM program can help to plan, program, and budget
    Real property inventory
    RPI & RPAM are functional level of a organization

## Slide 73: Summary (1 of 3)
LEED is a worldwide green building certification program developed by the USGBC or U.S. Green Building Council. USGBC developed LEED to include a set of rating systems for the design, construction, operation, and maintenance of green buildings, homes, and neighborhoods.
Buildings can qualify for 4 LEED certification levels:
  Certified: 40–49 points
  Silver: 50–59 points
  Gold: 60–79 points
  Platinum: 80 points and above
LEED-certified buildings use between 11 and 39% less site energy than non-LEED buildings, which reduces their ecological footprint, which is the impact of a person or community on the environment, expressed as the amount of land required to sustain their use of natural resources.

## Slide 74: Summary (2 of 3)
The LEEDs credit weighting process has the following 3 steps:
  Collection of reference buildings are used to determine environmental impacts of any building seeking LEED certification
  National Institute of Standards and Technology weightings are used to judge the importance of these impacts in each category.
  Data regarding actual impacts on environmental and human health are used to assign points to individual categories and metrics.
This LEEDs credit weighting process results in an average for each rating scheme based upon actual impacts and the importance of those impacts to health and environmental quality.
A green roof is a living building roof that is partially or completely covered with vegetation and a growing medium, planted over a waterproofing membrane. It may also include additional layers such as a root barrier and drainage and irrigation systems.
A passive house is a rigorous, voluntary standard for energy efficiency in a building, reducing its ecological footprint, which can result in ultra-low energy buildings that require little energy for space heating or cooling.

## Slide 75: Summary (3 of 3)
Construction and demolition materials are materials left over at a construction, renovation or demolition site, like concrete, wood, drywall, asphalt shingles, asphalt pavement, and metal, which can be reused or recycled to promote sustainability.
Thermal control is used in almost all buildings to achieve this comfort level and environmental control.
Daylighting and sustainable electric lighting are important elements of sustainable design. The incorporation of daylight in the design of a building provides non-energetic benefits. Daylighting increases in productivity and reduces dependence on fossil fuels. Sustainable lighting like LED and CFL can reduce the consumption of electricity
CMMS (Computerized Maintenance Management System) or computerized maintenance management information system (CMMS) is a software package that maintains a computer database of information about maintenance operations known as CMMIS (Computerized Maintenance Management Information System) used to verify regulatory compliance.