## Slide 1: Sustainability- Principles and Practices
Chapter 8
Solar Electric Generation

## Slide 2: LEARNING OBJECTIVES
Explain how photovoltaics (PV) create electricity from the sun.
Explain the difference in cost vs benefits of a PV system compared to a CSP system.
Discuss the Energy payback time (EPBT) of solar electric generation.
Describe energy returned on energy invested (EROEI) of solar.
Explain levelized cost of electricity (LCOE).
Describe grid parity.
Discuss grid integration.

## Slide 3: INTRODUCTION 1.
Solar Energy
  Promising form of renewable energy
    Without sun earth would not exist
    2 forms of solar electric generation
      PV (photovoltaics)
        Direct conversion of light into electricity, solar panels
        Used at private residences & large installations.
      CSP (Concentrated Solar Power)
        Uses focused sunlight and generates electric power
        Using mirrors to concentrate (focus) sun's energy
        Convert it into heat to power a steam generator

## Slide 4: PHOTOVOLTAICS (PV) 2.
Photovoltaics (PV)
  Production of electric current at interface
    Using 2 semiconductor materials
    Causes them to absorb photons of light
    Release electrons to produce electricity
  Conversion of light into electricity using semiconductors
    Photovoltaic effect as electrical current being produced
    Junction of light and semiconductors
Explained: Photovoltaics: 4:28

## Slide 5: Figure 8-1 Photovoltaic Solar Cell: Photovoltaics is direct conversion of light into electricity at atomic level. Certain materials exhibit a property known as photoelectric effect that causes them to absorb photons of light and release electrons. When free electrons are captured, electric current results that can be used as electricity

## Slide 6: PHOTOVOLTAIC PV CELL

## Slide 7: FREQUENTLY ASKED QUESTION?
Who Invented Photovoltaics?
  The photoelectric effect was first listed by a French physicist, Edmund Bequerel, in 1839, who discovered that certain materials would produce small amounts of electric current when exposed to sunlight. Albert Einstein described nature of light and photoelectric effect on which photovoltaic technology is based, for which he won a Nobel Prize in physics in 1905. The first photovoltaic module was developed by Bell Laboratories in 1954. It was promoted as a solar battery and was too costly for common use. NASA (National Aeronautics & Space Administration) began first serious use of the technology to provide power aboard spacecraft in sixties. Through the efforts of NASA and advanced technology, dependability of photovoltaics was established, and costs began to go down. Photovoltaic technology has gained recognition as a source of power during the oil embargo of the seventies.

## Slide 8: PHOTOVOLTAICS (PV) 3.
Photovoltaic (Photoelectric Cell) Operation
  In a solar cell, a thin semiconductor wafer
    Forms an electric field
  Positive on one side & negative on the other
  Light strikes cell, electrons are loosened from atoms
  In semiconductor material N-type and P-type wafers
  Electrical circuit formed so electrons can develop
  Current to turn on light bulb

## Slide 9: FIGURE 8-2 shows the operation of a basic photovoltaic cell, which is also called a solar cell. Solar cells are made from semiconductor materials, such as silicon that has been used in the electronics industry for decades with the invention of the transistor in 1946.

## Slide 10: FIGURE 8- 3 photovoltaic device single junction, which creates an electric field within a PV cell semiconductor. PV cell single-junction only produces photons whose energy is equal to or greater than 0 voltage section of cell (band gap) that can free an electron for circuit to flow. The photovoltaic reply of single-junction cell is limited to portion of sun's spectrum whose energy is above bandgap of absorbing material.

## Slide 11: FIGURE 8-4 The multi-junction device is a stack of individual single-junction cells in descending order of bandgap.

## Slide 12: QUESTION 1:
Which of these is defined as the production of electric current at the interface of two semiconductor materials?
a. Grid parity
b. Photovoltaics
c. Grid integration
d. Concentrating Solar Power

## Slide 13: ANSWER 1:
Photovoltaics

## Slide 14: PV (PHOTOVOLTAIC) SYSTEM 1.
Photovoltaic System Uses Solar Panels
  Number of solar cells that generate electrical current
  Pushed by voltage to become electrical power
  1st Step photoelectric effect
  Followed by an electrochemical process
    Crystallized atoms, ionized in a series
    Generate an electric current
    Ground-mounted, rooftop mounted or wall mounted
Residential Solar PV Economics: 49:20

## Slide 15: Figure 8-5 Solar Panel Array

## Slide 16: FIGURE 8-6 Solar cells in a frame called a photovoltaic module. These modules are designed to supply electricity. The current produced by module is dependent on how much light strikes it. Multiple modules are wired together to form an array. The larger the area of a module or array, the more electricity will be produced.

## Slide 17: PV (PHOTOVOLTAIC) SYSTEM 2.
DC Electricity
  Photovoltaic modules and arrays produce
  DC (direct-current) electricity
  Inverter is used to change the DC to AC
  Connected in both series and parallel arrangements
  Produce any required voltage & current combination
Payback for a Solar Panel System: 3:03

## Slide 18: PV (PHOTOVOLTAIC) SYSTEM 3.
Concentrator Photovoltaics (CPV)
  Use solar trackers and cooling system
  Increase their efficiency
  HCPV (high concentrator photovoltaics)
    Highest efficiency of all existing PV technologies
    Smaller array also reduces the balance of costs
    CPV not used in PV rooftop segment
    Areas with high direct normal irradiance of
      2000 khrs per square meter or more
      Electricity cost in range of $0.08–$0.15 per kilowatt-hour

## Slide 19: STUDENT ACTIVITY 3.
Download WORD file: EROEI (Energy Returned on Energy Invested) of Activity 1

## Slide 20: CSP (CONCENTRATING SOLAR POWER) SYSTEM 1.
Solar Power
  Transformation of sunlight into electricity
    Directly using PV (photovoltaics)
    Indirectly using concentrated solar power
Concentrated Solar Power Systems
  Use lenses or mirrors and a tracking system
  Focus a large area of sunlight into a small beam

## Slide 21: FIGURE 8-7 All CSP technological approaches require large areas for solar radiation collection when used to produce electricity at commercial scale. The 392 MW (Megawatt) plant Ivanpah in California. 392 Megawatt plant is a power tower system is the largest concentrating solar power plant in the world,

## Slide 22: FIGURE 8-8 Concentrating Solar Power (CSP): trough system Power Tower System and dish/engine system
CSP
  3 different approaches to solar energy:
    Power Tower Systems
    Trough Systems,
    Dish/Engine Systems

## Slide 23: CSP (CONCENTRATING SOLAR POWER) SYSTEM 2.
Solar Power Tower
  Dual-axis tracking reflectors (heliostats/Fresnel reflectors)
    Concentrate sunlight on central receiver tower
    Uses sea water heated to 932–1,832 ° F
    Stored in steam drum as heat source for power generator turbine
Figure 8-9 Solar Power Tower

## Slide 24: FREQUENTLY ASKED QUESTION?
What is some of the History of Solar Energy?
  A legend has it that Archimedes used a "burning glass" to concentrate sunlight on invading Roman fleet and repel them from Syracuse. Dr. Ioannis Sakkas, a Greek scientist performed an experiment in 1973 to see if Archimedes could have destroyed Roman fleet in 212 BC. He lined up 60 Greek sailors, each holding an oblong mirror tipped to catch the sun's rays and direct them at a tar-covered plywood silhouette 160 feet away. Ship caught fire after a few minutes. Auguste Mouchout in 1866 used a parabolic trough to produce steam for the first solar steam engine. The first solar-power system using a mirror dish was built by Dr. R.H. Goddard.

## Slide 25: FIGURE 8-10 The CSP parabolic trough consists of a linear or straight line parabolic (Parabola Shape) reflector that concentrates light onto a receiver positioned along the reflector's focal line

## Slide 26: CSP (CONCENTRATING SOLAR POWER) SYSTEM 3.
Parabolic Trough
  Receiver is a tube directly above middle
  Parabolic mirror and filled with sea water
  Reflector tracks along a single axis to follow
  Sun during daylight hours
  Sea water heated to between 300–660 °F
  Flows through receiver and becomes
  Heat source for power generator turbine engine.

## Slide 27: CSP (CONCENTRATING SOLAR POWER) SYSTEM 4.
Dish/Engine Systems
  Stand-alone parabolic reflector
    Concentrates light on receiver
    Positioned at reflector's focal point
    Reflector tracks sun
    Receiver working fluid is heated to 480–1,300 °F
    Used by Stirling engine to generate power
Figure 8-11 Dish Engine Systems

## Slide 28: FIGURE 8-12 Sterling engine is a heat engine that operates by cycled compression & expansion of a permanent gaseous fluid at different temperatures, so there is a conversion of heat energy to mechanical work. It is a closed-cycle regenerative heat engine with a permanently gaseous working fluid.

## Slide 29: COST BENEFITS OF PV SYSTEM COMPARED TO CSP SYSTEM 1.
CSP (Concentrating Solar Power)
  Old fashioned technology borrowed from coal plants
  Produce gas to drive a turbine
  2010 PV: global installed capacity of about 35 Gigawatts
  CSP had 1.5 Gigawatts.

## Slide 30: FIGURE 8-13 Megawatt Analysis of PV vs. CSP

## Slide 31: COST BENEFITS OF PV SYSTEM COMPARED TO CSP SYSTEM 2.
Two Reasons for Ascendency of
  Photovoltaics over Concentrating Solar Power:
    Market Size
    Technology

## Slide 32: FIGURE 8-14 Venture Capital and Private Equity investment in PV and CSP (2010/2011)

## Slide 33: CSP (CONCENTRATING SOLAR POWER) SYSTEM 3.
PV vs. CSP
  Photovoltaics (PV) installed almost everywhere
  CSP can be installed, reverse is not true
    CSP technology needs higher levels of irradiance
    Large-scale distributions like 20 Megawatts
  PV (Photovoltaics) centers on solar cell
  CSP is collection of sophisticated components

## Slide 34: CSP (CONCENTRATING SOLAR POWER) SYSTEM 4.
EPBT (Energy Payback Time)
  Time required to generate as much energy
  As is consumed during production/lifetime of system
  Payback time has been decreasing
  2000, PV energy payback time for PV 8 to 11 years
  2006 1.5 to 3.5 years for crystalline silicon PV systems
  2013 dropped to 0.75–3.5 years.
Energy Return on Investment: 2:04

## Slide 35: QUESTION 2:
Which of these uses three different approaches to solar energy: power tower systems, trough systems, and dish/engine systems ?
a. Grid parity
b. Concentrating Solar Power
c. Grid integration
d. Photovoltaics

## Slide 36: ANSWER 2:
Concentrating Solar Power

## Slide 37: STUDENT ACTIVITY 2.
Download WORD file: EPBT (Energy Payback Time) of Activity 1

## Slide 38: CSP (CONCENTRATING SOLAR POWER) SYSTEM 5.
EROEI (Energy Returned on Energy Invested)
  Ratio of electricity generated divided by
  Energy required to build and maintain equipment
    EROEI uses the following formula:

## Slide 39: QUESTION 3:
Which of these solar systems offers higher efficiency and better energy storage capability?
a. Dish/engine
b. Photovoltaics
c. Trough
d. Power tower

## Slide 40: ANSWER 3:
Power tower

## Slide 41: STUDENT ACTIVITY 1.
Download WORD file: Cost Benefits PV (Photovoltaics) System vs. CSP (Concentrating Solar Power) System

## Slide 42: GRID PARITY 1.
Grid Parity
  Alternative energy source that can generate power
    At LCOE (Levelized Cost of Electricity)
    < or equal to price of buying power from local utility grid
    LCOE is generally used when discussing
    Renewable energy sources, like solar and wind power
    Grid parity depends upon whether you calculate
    From view of a consumer or power utility

## Slide 43: STUDENT ACTIVITY 4 .
Download WORD file: Grid Parity

## Slide 44: FIGURE 8-15 path to grid parity

## Slide 45: GRID PARITY 2.
Reaching Grid Parity
  Point at which an energy source becomes
  Competitor for widespread development
  Pricing of electricity from the grid is very complex
    Utility providing power
    Utility delivering power
      Often separate bodies who enter into an agreement
      Sets fixed rate for all of the power delivered
Grid Parity: 4:01

## Slide 46: GRID INTEGRATION 1.
Grid-Integrated Photovoltaic Power System
  Electricity generating solar PV power system
    Connected to utility grid
    Consists of solar panels, inverters, a power conditioning unit
    Grid connection equipment
    Small residential and commercial rooftop systems to
    Large utility-scale solar power stations
    Grid-connected photovoltaic system supplies excess power
Redefining What’s Possible: Grid Integration: 3:21

## Slide 47: FIGURE 16 PV Grid Integration with Utility Grid

## Slide 48: Electrical Energy Distribution

## Slide 49: GRID INTEGRATION 2.
Typical System
  Systems with more than a10 kilowatt capacity
  Meet load of most customers
  Supply excess power to the grid
  Consumed by other users
  Meter is used to monitor power transferred
  If PV wattage exceeds average consumption
  Produce revenue by selling the power back to utility

## Slide 50: QUESTION 4: ?
Which of these is the time requisite to generate as much energy as is consumed during the production and lifetime operation of the energy system?
a. EPBT (energy payback time)
b. EROEI (Energy Returned on Energy Invested)
c. LCOE (Levelized Cost of Electricity)
d. LEC (Levelized Energy Cost)

## Slide 51: ANSWER 4:
EPBT (energy payback time)

## Slide 52: LCOE (LEVELIZED COST OF ELECTRICITY) 1.
The LCOE (Levelized Cost of Electricity)
  Measure of a power source
  Compare different methods of electricity generation

## Slide 53: FIGURE 8-17 shows a comparison of LCOE across energy sectors. LCOE is an economic assessment of average total cost to build & operate a power-generating asset over its lifetime divided by total energy output of asset over that lifetime.

## Slide 54: LCOE (LEVELIZED COST OF ELECTRICITY) 2.
LCOE Cost Factors:
  Capital costs (waste disposal) -low for fossil fuel power stations; high for wind turbines, solar PV; very high for waste to energy, wave and tidal, solar thermal, and nuclear
  Fuel costs - high for fossil fuel and biomass sources, low for nuclear, and zero for many renewables
    Factors such as costs of waste and different insurance costs are not included in works power or parasitic load or portion of generated power actually used to run station's pumps and fans.

## Slide 55: LCOE (LEVELIZED COST OF ELECTRICITY) 3.
Formula for LCOE is listed below:
Solar: LCOE: 12:49

## Slide 56: LCOE (LEVELIZED COST OF ELECTRICITY) 4.
Factors Affecting LCOE
  Electricity price
  Adjusting for inflation
  Process improvements
  Average retail price of equipment

## Slide 57: QUESTION 5:
Which of these is a measure of a power source which tries to compare different methods of electricity generation on an equivalent basis?
a. EPBT (energy payback time)
b. EROEI (Energy Returned on Energy Invested)
c. LCOE (Levelized Cost of Electricity)
d. LEC (Levelized Energy Cost)

## Slide 58: ANSWER 5:
LCOE (Levelized Cost of Electricity)

## Slide 59: Summary (1 of 4)
Photovoltaics or just PV is defined as the production of electric current at the interface of two semiconductor materials, which causes them to absorb photons of light and release electrons to produce electricity and is a form of renewable energy
PV concerns the conversion of light into electricity using semiconducting materials that exhibit the photovoltaic effect as electrical current being produced at the junction of light and a semiconductor or the use of solar (sun based) energy.
In a solar cell, a thin semiconductor wafer is used to form an electric field, positive on one side and negative on the other. When light strikes the solar cell, electrons are loosened from the atoms in the semiconductor material N-type and P-type silicon wafers. With electrical conductors attached to the positive and negative sides, an electrical circuit is formed so the electrons can develop an electric current.

## Slide 60: Summary (2 of 4)
Solar cells are electrically connected to each other and mounted in a frame is called a photovoltaic module. The current produced by a module is directly dependent on how much light strikes the module. Multiple modules can be wired together to form an array.
Multiple solar modules are wired together to form an array. The larger the area of a module or array, the more electricity will be produced. Photovoltaic modules and arrays produce DC electricity. Inverters used to change the DC to AC.
PV Installations may be ground-mounted, rooftop mounted or wall mounted.
Concentrating Solar Power (CSP) technology uses three alternative technological approaches: power tower systems, trough systems, and dish/engine systems.

## Slide 61: Summary (3 of 4)
The high efficiency of PV systems reduces the balance of system costs. For areas with a high annual direct normal irradiance of 2000 kilowatt-hours per square meter or more, the cost of electricity is in the range of $0.08–$0.15 per kilowatt hour and installation cost for a 10-megawatt CPV power plant is about $1.50-$2.30 per watt peak.
In 2010 PV had a global installed capacity of approximately 35 Gigawatts, compared with CSP’s 1.5 Gigawatts. There are two reasons for the ascendency of Photovoltaics over Concentrating Solar Power:
Photovoltaics (PV) can be installed almost everywhere that Concentrating Solar Power (CSP) can be installed, but the reverse is not true. CSP technology needs higher levels of irradiance, access to water, and large-scale distributions like 20 Megawatts or more compared the small amount of kilowatts in a residential PV system.

## Slide 62: Summary (4 of 4)
The energy payback time (EPBT) of a power generating system is the time required to generate as much energy as is consumed during production and lifetime operation of the system.
EROEI (energy returned on energy invested) is the ratio of electricity generated divided by the energy required to build and maintain the equipment.
Grid parity is an alternative energy source that can generate power at a LCOE (Levelized Cost of Electricity) that is less than or equal to the price of purchasing power from the electricity grid.
A grid-integrated photovoltaic power system is an electricity generating solar PV power system that is connected to the utility grid.
LCOE (Levelized Cost of Electricity) is a measure of a power source which attempts to compare different methods of electricity generation on a comparable basis.